## Slide 1: FortiExtender
Product Overview

## Slide 2: Background
FortiGates have previously relied on USB modem or embedded modems for 3G/4G Wireless WAN connectivity
The FortiGate is usually located in back office or wiring closets
This is not well located for optimal 3G/4G reception

## Slide 3: FortiExtender Solution
FortiExtender
Extend 3G/4G modem with external device
  Allow optimal placement to increase signal to noise ratio
  eg. Near a window or outdoors.
Managed and configured by FortiGate
  As primary WAN connection
  As failover WAN connection for redundancy
Connected to FortiGate via Power over Ethernet (PoE)

## Slide 4: Connectivity
Ethernet connection
CAPWAP tunnel created between FortiGate and FortiExtender for all control and data traffic
FortiExtender appears as a WWAN (not modem) port in FortiOS
PoE is required on some models

## Slide 5: FortiOS FortiExtender Overview
Requires FortiOS 5.2
Available on all FortiGate models
Management and configuration
  Modem Configuration Settings
  Modem Line Status
  Firmware Upgrade
Monitoring
  Extender Detection, Modem Detection, WAN Service Status, Current/Monthly Data Usage

## Slide 6: FortiOS FortiExtender Setup
Discovery – Auto or manual (for routed networks)
Similar to adding a FortiAP
Device Authorization
Comprehensive Modem settings on GUI

## Slide 7: FortiExtender Operation
Diagnostic Tools
Ping, AT Commands
Primary and secondary modems
Daily/Monthly Usage Monitoring
Signal Strength Monitoring

## Slide 8: FortiExtender-100B
Qualified Modem & Antennas Supplied by Customer
IP55 rated enclosure
Ruggedized for use in outdoor and harsh environments
PoE powered (injector included)
USB modem and antenna to be supplied by user
Now
ISP | Modem | Brand
AT&T | AC340 | Netgear (Sierra)
AT&T | AC341 | Netgear (Sierra)
Verizon | USB551L | Novatel
Sprint | AC341U | Netgear (Sierra)
Initial Modem Support:

## Slide 9: The Fortinet Advantage
Single pane of glass management for your infrastructure
Simplifies deployment and reduces TCO
Remote monitoring of devices
No need to purchase cloud based subscription to check status
Automatic discovery and software upgrade
Easy to deploy and manage

## Slide 10: FAQs
Is there any requirement to console or access directly into FortiExtender?
The FortiExtender automatically discovers a FortiGate using CAPWAP protocol much in same way a FortiAP automatically discovers FortiGate. There is no need to manage or configure the FortiExtender via its console port.
How are they powered?
FortiExtender-100B model can only be powered via PoE. The injector and injector power supply are included with the product.

## Slide 11: FAQs
Are there other accessories that is included?
Pole mount kit is included.
How does one qualify a new modem that is not listed?
Identify the latest supported modems via FortiOS release notes.
Only contemporary modems are supported. Many older modems have gone EOL by manufacturers and will not necessarily be supported by default.
Additional modem support can be requested via established feature request process.
Are external antennas supported?
Yes, there is some room to house small antennas. If it’s to large, there’s provision to extend it to another 3rd party chassis.

## Slide 12
Q & A